## Slide 1
3.3 Connect electrodes and HPIs
3.4 Check subject comfort
1.1 Check or adjust MEG gantry position
1.2 Verify safe gantry position
1.3 Connect and switch on stimulus equipment
1.4 Verify that stimulation settings and intensities are correct
1.5 Check MEG sensors, heat if needed.
1.6 Check experiment triggers
1.7 Create or check project and acquisition settings.
1.8 Make empty room recording
2.1 Welcome subject
2.2 Inform subject about the experiment
2.3 Collect & sign written consent
2.4 Subject changes clothes
2.6 Attach electrodes and check electrode impedance
2.7 Attach HPI coils
2.8 Digitize HPI coils and head shape. Save preparation.
2.9 Instruct subject
3.1 Create / or load project and acquisition settings. Load preparation.
4.1 Begin recordings
3.7 Check MEG sensors, heat if needed
4.3 Make lab notes
3.2 Seat subject comfortably and in optimal position inside MEG helmet
3.8 Check MEG, EOG, ECG MISC, TTL, buttons, etc
3.9 Check for artefacts
4.8 Save data with your initials
3.6 Check HPI measurements
5.1 Move subject out of MEG helmet
5.2 Detach electrodes + HPI
5.6 Clean HPIs
5.7 Clean up MEG and MSR
5.8 Clean up MEG lab
5.9 Clean up changing room
5.3 Debrief subject
MEG MEASUREMENTS
MAIN PROCESS
SUB PROCESSES
ACTIVITIES
2.0 PREPARING SUBJECTS
1.0 PREPARING EQUIPMENT
3.0 PREPARING MEASUREMENTS
4.0 DOING MEASUREMENTS
5.0 AFTER MEASUREMENTS
4.4 Monitor subject comfort
4.5 Monitor and assess subject sleepiness
5.11 MaxFilter MEG data and upload filtered data, if applicable.
5.11 Delete your uploaded data
2.5 Add subject to database
4.7 Monitor stimulus procedure / protocol progress
3.5 Check bubble, 2-way communication & camera
3.10 Make sure subject's head is in best position for recordings
2.10 Give subject safety instructions
4.6 Monitor signal integrity
4.9 Complete lab notes
5.4 Subject changes back clothes
5.5 Thanks and goodbye to subject
5.10 Organize and upload your data, from DACQ and other
4.2 Initiate stimulus procedure / protocol
Notes: 1